## Slide 1
Module 2: Measurement
Measuring and Analyzing Network Traffic
ML for Cybersecurity
Fall 2020

## Slide 2: Learning Objective

## Slide 3: Learning Objectives
Describe different considerations and approaches to measuring Internet traffic in a sound way
Collect network traffic using a variety of industry-standard tools and packages
Represent the network data that has been collected in ways that can be inputted into machine learning models.
Load the data into software libraries for analysis and modeling.

## Slide 4: Measurement and DATA Collection

## Slide 5: “You Can’t Improve What You Don’t Measure.”

## Slide 7: What Data Can Tell Us About Networks
Security (This Course)
  Detect and mitigate attacks
  Determine source of attacks
  Identify unusual behavior
  Identify devices
Performance and Reliability
  Diagnose performance and reliability problems
  Plan provisioning, detect customer problems, …

## Slide 9: Types of Network Measurements (with demonstration)
traceroute
ping
UDP “probes”
TCP probes
Application-level probes
  Web downloads
  DNS queries
Packet traces
  Complete
  Headers only
  Specific protocols
Flow records
Specific data
  Syslogs …
  HTTP server traces
  DHCP logs
  Wireless association logs
  DNSBL lookups
  …
Routing data
  BGP updates / tables, ISIS, etc.
Passive
Active

## Slide 10: Before Machine Learning: Data Quality!
Cross-validation
  consistency checks
  Multiple independent measurements of the same phenomenon
  Database queries can be a useful tool
Other considerations
  Anonymization and privacy
  Maintaining longitudinal data

## Slide 11: Measuring Network Traffic: Two Main Approaches
Packet-level Monitoring
  Keep packet-level statistics
  Examine (and potentially, log) variety of packet-level statistics. Essentially, anything in the packet.
  Timing
Flow-level Monitoring
  Monitor packet-by-packet (though sometimes sampled)
  Keep aggregate statistics on a flow

## Slide 12: Packet Capture: tcpdump/bpf
Put interface in promiscuous mode
Use bpf to extract packets of interest
Packets may be dropped by filter
  Failure of tcpdump to keep up with filter
  Failure of filter to keep up with dump speeds
Question: How to recover lost information from packet drops?
Accuracy Issues

## Slide 13: Traffic Flow Statistics
Flow monitoring (e.g., Cisco Netflow)
  Statistics about groups of related packets (e.g., same IP/TCP headers and close in time)
  Recording header information, counts, and time
More detail than SNMP, less overhead than packet capture
  Typically implemented directly on line card

## Slide 14: What is a Flow?
Source IP address
Destination IP address
Source port
Destination port
Layer 3 protocol type
TOS byte (DSCP)
Input logical interface (ifIndex)

## Slide 15: IPFIX (Cisco Netflow, Sflow, etc.)
Basic output: “Flow record”
Newer versions have:
  More flexible record format
  Much easier to add new flow record types
Core Network
Collection and Aggregation
Collector (PC)
Approximately 1500 bytes
20-50 flow records
Sent more frequently if traffic increases

## Slide 16: What is in a Flow Record?
Source and Destination, IP address and port
Packet and byte counts
Start and end times
ToS, TCP flags
Basic information about the flow…
…plus, information related to routing
Next-hop IP address
Source and destination AS
Source and destination prefix

## Slide 17: Aggregating Packets into Flows
flow 1
flow 2
flow 3
flow 4
Criteria 1: Set of packets that “belong together”
  Source/destination IP addresses and port numbers
  Same protocol, ToS bits, …
  Same input/output interfaces at a router (if known)
Criteria 2: Packets that are “close” together in time
  Maximum inter-packet spacing (e.g., 15 sec, 30 sec)
  Example: flows 2 and 4 are different flows due to time

## Slide 18: Demonstration: Packet Capture in Python

## Slide 20: Start: Example Basic Analysis Questions
How many devices are on the network?
What are the most common destinations?
How much traffic is each of the devices sending?
  In total?
  To each destination?